## Slide 1: Møller Polarimetry Update Don Jones Temple University
December 2021 :: MOLLER Collaboration Meeting

## Slide 2
Agreement with Compton at ±0.02% level
0.2%
0.5%
CREX Results
Møller and Compton measurements during CREX

## Slide 3
Record accuracy for JLab Møller polarimetry.
Significant progress has been made on Azz systematic.
It looks like we will be able to reach 0.14% or better uncertainty for Azz at 11 GeV.
CREX Systematics Results

## Slide 4
Limiting the vertical detector acceptance allows AND over-tuning past rate peak to pull electrons off dipole walls allowed us to tune the Levchuk correction to nearly zero AND create a large flat region of Azz.
1.3%
Simulated Azz
Levchuk Corr Azz
Coincidence Rate
Simulated Azz
Levchuk Corr Azz
Coincidence Rate
Quadrupole 1 Detuning %
Moller Azz: Two Recent Improvements
Our knowledge of spectrometer optics (field maps) is limited to several percent uncertainty, BUT simulation shows if we calibrate our settings relative to the rate maximum, we are highly insensitive to absolute knowledge of optics.
PREX 2 PMT Simulation
PREX 8 PMT Simulation
Quadrupole 1 Detuning %
Relatively Flat Azz Region
Active PMTs (Red)
Active PMTs (Red)

## Slide 5
Coincidence Rate
Simulated Azz
Levchuk Corr Azz
At 11 GeV, with current beamline setup, we are unable to tune away large Levchuk correction nor create a flat region insensitive to accurate knowledge of the optical tune
However, moving target 30 cm upstream accomplishes what we want by allowing Moller scatters to further separate before quadrupole steering. Now officially implemented in beam line design.
Caveat: results for 4.5cm vertical detector acceptance.
May require detector redesign or collimator.
Azz at 11 GeV optics
Coincidence Rate
Levchuk Corr Azz
Simulated Azz

## Slide 6
Moving Møller target coils upstream required some re-configuring of the beam line design: design changes now included in model
Plan in place to implement improved MOLLER beam line including Møller target move before MOLLER
  Could be as early as Spring 2022, although the probability for getting all parts in hand on time is low.
  Early implementation gives us time to study impact of redesign and benchmark simulation ahead of time.
Beam Line Redesign Being Implemented

## Slide 7
Levchuk correction requires a model of the momentum distributions for polarized and unpolarized electrons in Fe
For past two decades this correction has been done using distributions from modified hydrogen wavefunctions.
Data from CREX showed that this calculation predicted a 30% smaller “peak” than measured.
Reached out to expert John Perdew⃰ at Temple University and his student Aaron Kaplan suggested a Hartree-Fock model and provided the momentum distributions.
 Exciting agreement! 
⃰ John Perdew is one of the most highly cited scientists of all time with over 150,000 Google citations
Another recent improvement for Azz
Hartree-Fock Model
Modified Hydrogen Model
CREX Data

## Slide 8
Systematics inflated by foil polarization and high current extrapolation
These two contribute a total of 0.76% and the rest is 0.38%
Likely overestimated (given level of agreement with Compton which had 0.5% uncertainty) but difficult to limit without better measurements
CREX Troublesome Systematics

## Slide 9
Potential to be the limiting systematic unless we measure it.
We will develop a plan to directly measure:
  Beat frequency method used before where the laser is tuned just off the 499 MHz so only every nth pulse actually goes to the hall but full power on photocathode.
  Can investigate what statistics Compton could get at 5 uA for 8 hrs.
Extrapolation to High Current

## Slide 10
Potentially large systematic: 1% smaller polarization during PREX-2 when running on a wrinkle
Attempts to measure with Kerr apparatus only partially successful.
Kerr apparatus: modulate polarization at fixed frequency and pull out polarization signal on reflected light from magnetized foil with lock-in amplifier (magnetization rotates polarization)
Publication nearly ready to submit to NIM that shows Fe foil polarization at saturation known to ±0.24%
Still need to prove that we are at saturation
Sensitivity of degree of saturation on foil and angle and flatness needs to be measured
Foil Polarization

## Slide 11
Example saturation curves taken with Kerr apparatus
Not able to conclusively reach saturation but see signature of interference effects.
Longer careful study required but may not be possible.
Need to develop plan for using beam to set upper limit on this systematic
Kerr Apparatus

## Slide 12
GEMs are being installed between the dipole and the detector to help verify simulated radiative, Levchuk and multiple scattering effects.
Design recently completed by Nilanga’s group at UVA -- ready for construction
Readout split into right and left required to allow for resolution of left and right coincident Moller electrons
Support structure design to start soon
GEMS for the Møller Polarimeter

## Slide 13
Addition of a collimator is part of the project to help limit systematics
Need more simulation work to decide if this is needed and what its design should be.
  Initial investigation underway
May be required to limit vertical acceptance on detector (remove sensitivity to Levchuk and knowledge of quad optics settings)
Target date set to make design decision by early April
Collimator

## Slide 14
Møller Polarimetry Active Personnel
Donald Jones | Jim Napolitano | Eric King
Paul Souder | Faraz Chahili
David Gaskell | Simona Malace | Bill Henry
Kent Paschke
Working on GEM insights.
GEM event reconstruction of simulated events.
Maintain hardware.
Coordinate project deadlines.
Technical operators.
Working on polarized materials review.
Continued systematics reduction.
Reviewing design issues.
Insight
Advice

## Slide 15
Encouraging progress made on systematics during PREX-2 and CREX
Progress on Azz & Levchuk systematics nearly meet MOLLER requirements
Two systematics (foil polarization and high current extrapolation) are highest priorities and will likely require beam time to limit
Progress is being made on hardware improvements included in the MOLLER project, with
  GEM design complete and support structure design to begin soon
  Collimator design choice made by early Spring.
All systematics being reviewed carefully
Summary