## Slide 1: PQB Update
MOLLER Accelerator Tasks and Injector Upgrade
Riad Suleiman
MOLLER Collaboration Meeting
June 22, 2022

## Slide 2: MOLLER Accelerator Tasks
Fast Helicity Reversal:
  Ordered 6-8 Helicity new Generator Boards (to be ready by August)
  Ownership will be transferred to Fast Electronics and DAQ Group
  MOLLER Settings: Free Clock Mode, 1920 Hz, 510.85 µs T_Stable,10 µs T_Settle, three 64-window patterns, 128-window delay.
  Request was sent to Engineering Division (EESICS) – new boards will come with new firmware
Helicity Decoder Boards:
  Two protypes are under testing (UITF Mott and Hall B), 20 boards are on order
  Re-visit firmware to ensure no possibility of real helicity decoding on board, only after event readout
Laser Table Jobs
  New RTP HV Driver:
    Continue to use RTP (pare: KD*P)
    Build new RTP HV Driver: define effort between JLab & UVa (NSF funded) and implement Caryn’s comments
  Upgrade IA system
    4th channel for Hall D (need Hall D parity DAQ)
    Reduce transition time <10 µs

## Slide 3: MOLLER Accelerator Tasks … cont’d
Complete Injector Upgrade
  Phase-I beam line installed last year (see Caryn’s talk from Jun 2021 Collab. Meeting)
  Building new 200 kV gun (based on successful 350 kV gun) to eliminate FE
    Tilted anode to eliminate vertical kick inside gun
    Biased anode to prolong lifetime/keep QE uniform
  Booster commissioning at UITF was successfully completed
  Phase-II Booster installation planned for next SAD (March-May 2023)
  Afterwards, assessment of adiabatic damping and charge asymmetry for high current (less clipping, less x-y coupling)
Upgrade Helicity Magnets Control
  MOLLER will use magnets to study sensitivities to position differences, position feedback (to suppress beam jitter), and check adiabatic damping
  Request to upgrade was submitted to EESICS
  Need to identify new owner from EESICS
  MOLLER to provide a requirement document by end of summer 2022 (include quadruple magnets for beam size?)
Feedback on Horizontal Polarization Orientation
  Options considered: use H-Wien, new air-core short Wien in keV region, or new air-core long Wien in MeV region
  MOLLER to provide a requirement document by end of summer 2022

## Slide 4: MOLLER Accelerator Tasks … cont’d
Develop/Test 20 Amp low-noise trim for Wien magnets
  Wien magnets have too low inductance for 20 Amp SCE power supplies to regulate well
  DC Power Group to design/test 20 Amp low-noise trim card for 2023 March SAD
Halo monitors in Hall A and beam studies at 11 GeV
  On MOLLER collaboration to-do list
Study co-operation of MOLLER with KL experiment in Hall D
  Requires low rep rate, low average current - 7.8 MHz, 5 µA average current, any issues?
  RF loading (?): explore beam loading of high bunch charge, i.e., 0.64 pC @ 7.8 MHz (128 ns) to Hall D at 5.5 pass (compared to 0.26 pC @ 249.5 MHz to MOLLER)
Need help from MOLLER to provide students and postdocs to support Injector activities and run parity DAQ