## Slide 1: Spectrometer Update
MOLLER Collaboration Meeting
21-22, June 2022
Juliette Mammei
Experimental Contact
University of Manitoba
[Supported by: the MOLLER collaboration, JLAB Magnet Group, MIT Magnet Group]

## Slide 2: Team Acknowledgements
JLAB Magnet Group
  Mike Bevins (CAM)
  Probir Ghoshal (Magnet Group Leader)
  Dave Kashy (Principal Mechanical Engineer –
  Spectrometer Lead)
  Eric Sun (Senior Mechanical Engineer)
  Sandesh Gopinath (Mechanical Engineer)
  Randy Wilson (Mechanical Designer)
  Dan Young (Mechanical Designer)
Physics Collaboration
  Juliette Mammei (Experimental Contact)
  Krishna Kumar
  Chandan Ghosh
  Sakib Rahman
  Nazanin Roshanshah
  Ciprian Gal
  Kent Paschke
  and others…
MIT Bates REC
  James Kelsey (Associate Director Bates)
  Ernie Ihloff (Principle Research Scientist)
  Jason Bessuille (Senior Mechanical Engineer)
  Danielle Petterson (Mechanical Engineer)
  Designer/ Draftsperson TBD
Damon Spayde – massive effort in shielding studies
Notes: Ruben sadly has left, he is now working on ITER at Princeton. I am happy to report he now thinks MOLLER is completely sane in comparison
We are very happy to announce that MIT is now finally back on board after settling contract issues; they will be taking over the upstream torus region, including the enclosure, supports and collimator 1+2 as well as the torus itself.

## Slide 3: Open Spectrometer system separates signal from backgrounds
Coils in one septant
Acceptance defining collimator
particle envelopes
along beamline
Beam pipe and enclosures
Bellows and supports
collimators to control backgrounds
Blockers to study backgrounds
Lintels and “collars” to shield coils and detectors
Field measurement system
Instrumentation and controls
Window separating target chamber from US enclosure target group
Spectrometer Elements
Set of resistive toroidal magnets (US and DS)
2 collimators to define the acceptance of the signal and that of the unscattered beam
US region MIT

## Slide 4: Upstream Region - MIT
All collimators are pure W or WCu; no nickel is permitted.
All will be housed in a vacuum chamber at 1x10-2 Pa
All except 2-bounce shield support own weight alone
Blocker Collimator
Cooled during operation
Sieve Collimator
Array of high-aspect ratio holes 1mm-10mm
Collimator 1-2
Complex 4-piece brazement with internal cooling passages
2-Bounce Shield
Long, self-supporting / structural piece
Collimator 4
500mm diameter, 500 kg

## Slide 5: Sieve and Blocker
Blocker used to study backgrounds
  Leave one septant open to study cross-talk?
Sieve holes to be used in optics calibrations
Pattern or hole sizes used to identify holes
Asymmetric placement so we can determine the orientation
10 cm thickness along z, need to take care with aspect ratios of holes
Moveable into and out of the beamline
Needs to be positioned accurately
Optics group will specify the size, number and angle (if any) of holes

## Slide 6: Conceptual ray drawing
Collimators
1+2 4
Inner Photon Envelope
ep
Target
Lintels
Collars
Detector plane
moller
Ray traces with apertures
All shown in one sector (coils are actually in closed sector)
Positions and sizes verified with simulations (taking into account radiative effects)
Rays for “primary beam” particles of different energies and angles
Moller/ep
Line of sight
Vertical axis centered at ~subcoil 4 entrance
DS beampipe between OPE and ep envelopes
Outer Photon Envelope

## Slide 7: Alignment tolerances
along z
radially
azimuthally
Tolerances determined by single coil/single offset studies have been verified with “worst-case” multiple coil/multiple offsets within the specified tolerances
Considerations
  physics optics (ability to “deconvolute” the asymmetries with desired uncertainty)
    signal electron focal plane distributions
    backgrounds
  clearance with the scattered particle envelopes
  clean transport to the dump
  doses on coils (epoxy, especially at inner radius)
Physics worst case
All coils offset in same direction (without us knowing)
Least likely (survey, tracking)
Relatively insensitive
single coil/ single offset tolerances
BEAM worst cases tested
coils aligned in a “conspiratorial” way within tolerances
→ induces dipole along beamline
worst (to left)
more likely - only ±0.5 mm
most likely ±0.5 mm and random for different subcoils

## Slide 8: Clean transport to dump
W/µA/(1mm x 1mm)
dump entrance
flange (r = 483 mm)
limiting aperture in dump tunnel (r=300mm)
(~0.5 m downstream)
Beampipe for SAMs
OD 400 mm
End of Hall
electrons
38.1 W
260 W
13.4 W
17.8 W
14.2 W
Symmetric coils, no SAMs
Case 1, no SAMs/shield
Symmetric coils, w/ SAMs
Case 2, w/ SAMs/shield
Case 3, w/ SAMs/shield
Integrated Power from 200 mm < r < 600 mm
Total Beam Power 715 kW
Coil Configuration
(most likely configuration)
worst-case (within tolerances)
Worst case scenario

## Slide 9: CTD Epoxy radiation tests
Chart: CTD 403 - S2 Strength vs Dose
| 0 | 40.5 | 83.9 | 124.4
Vacuum | 66.4 | 67.5 | 55.8 | 51
Nitrogen | 66.4 | 66 | 45.5
Unsheilded doses > 300 MGy
Goal stresses and doses (with factors of ~2)
*See Dave’s talk for details
Shielded doses ~50-100 MGy

## Slide 10: Epoxy shielding optimization (Upstream)
Geo 4, Slide 10
https://moller.jlab.org/DocDB/0008/000892/001/PhotonBackgroundsUpdate%20%282%29.pdf
Inner Radial Layer
Left side
Right Side
(Symmetric configuration shown)
Current Status:
Reducing the thickness of the 2-bounce shield tube without adversely affecting the spectrometer epoxy dose and photon backgrounds at the detector plane.
This will reduce the mass of the shielding tube and potentially also the power deposited in the tube itself.
Cutaway view from side
View from downstream
Coil epoxy encasing the conductors
2-bounce shield with cutouts for coils
W wedges

## Slide 11: Epoxy dose in DS with worst-case asymmetric map
Yes, that is
2.4 Giga-Gray!!!
Whatever shielding is designed needs to be capable of shielding the coils in a misaligned or asymmetric case
Plates on underbelly reduce this to ~ 100 MGy

## Slide 12: Epoxy shielding optimization (Downstream)
Current Status:
3 mm thick plates underneath coils in downstream (DS) 1, 2, 3 and 4
The plates are still being optimized for weight
Cutaway view from side
DS 3
DS 1
DS 2
DS 4
Bottom plates (3mm W) on every coil
Inner Radial Layer
Left side
Right Side
(Symmetric configuration, with bottom plates)
Geo 4, Slide 11
https://moller.jlab.org/DocDB/0008/000892/001/PhotonBackgroundsUpdate%20%282%29.pdf
w/o shielding, worst asymmetric map results in a dose of

## Slide 13: Dose on underbelly in DS
Symmetric, w/ shield
+/- 1 or 3 mm offset, w/ shield
+/- 0.5 mm offset, w/ shield
* “Kryptonite” stops all tracks that hit it.
Symmetric, no shield
Symmetric, Kryptonite* shield
+/- 1 or 3 mm offset, no shield
Are stresses high at same place where dose will reduce the strength?

## Slide 14: Modelling the as-built coils
Several ways to determine the positions of the conductor
Mechanical surveys
Tracking measurements
Field measurements – chance to adjust coils
Field measurements:
Perform the measurements during the magnet testing
Each individual magnet set (upstream, and DS 1-4)
Compare to calculations (TOSCA) for offset coils
Goal: minimize the dipole field in the bore
160 180 200
Azimuthal angle (degrees)
0 100 200 300 400
Radius (mm)
B (Gauss)
B (Gauss)

## Slide 15: Magnetic Field Measurements
Existing apparatus with motion mechanism used to successfully measure the field in the CLAS12 magnet
Probe can be moved along z for a given radial/azimuthal position
Will need longer tubes for the DS4
Every 5 cm along 2 m in z takes ~ 2 hours, with 2.5 hours to change
Modified plate for our desired locations
0 5 10 15 20
Distance from target center (m)

## Slide 16: Optimization of the positions
in the direction
azimuthal de-focusing
Vector map colors show relative total field strength in a septant
Radial components of field cause azimuthal (de-)focussing near the conductor at the (outer) inner radius of the conductor
  Provides required inelastic electron separation
  Causes mid-angle mollers to fill full azimuth at detector
Field varies along z to separate the low E moller and high E eps
z=9500mm
R=135mm
azimuthal focusing
Conductor and tube cross-sections approximately to scale
How many points along z do we need? How many ?
Notes: This contour plot shows the relative strength of the total field in different locations within a septant. The approximate locations of the adjacent coil cross-sections are shown in orange. Illustrative field vectors indicate the direction of the field at different places. The radially focussing part of the field is the phi component; at the center of the septant the field is all in the phi direction. Near the coils, however, you have components in the radial direction. In between the inner radius parts of the coil, this results in azimuthal focussing of electrons; in between the outer radius parts of the coils we get phi defocussing. We make use of the focussing in phi to study the different parts of the acceptance.

## Slide 17: Ongoing work (on physics side)
Optimizing the epoxy shielding
  Reducing weight
  Shielding where stresses and doses highest
  Ensuring it will work even with worst-case offset coils
Checking the energy deposition in layers
Optimizing the field measurement procedure
Simulations of the prototype coil (changes due to manufacturing)
Defining the system requirements (SRD)
Preparing for the TRD

## Slide 18: Appendix

## Slide 19
make a distortion using a shunt to compare to simulation

## Slide 20: Collimator system
Upstream region
Collimator 2 defines angular acceptance for signal
Collimator 1 inserted into 2 to shield end
Wedges and “2-bounce” tube to shield US torus epoxy
Downstream region
Collimator 4 has a similar profile to 2 – “cleanup collimator”
Collimators 5 and 6a, b provide additional clearance to coils
lintels and collars provide shielding

## Slide 21: Collimators 5 and 6a,b
Shielded
At the main detector
no Col 6a or b
at 6b location, with col 6a in place
US z=7547.93mm
DS z=7647.93 mm
Collimator 5
at 6a location

## Slide 22: Outstanding questions for physicists (from last meeting)
Field map and interpolation tests – our current maps are okay
  Extent – can/should it be smaller than 75 cm in the downstream?
  Coarseness of grid – probably okay; want to test the limits, optimize
  Interpolation – default is linear interpolation, investigating cubic as well
Dose reduction on epoxy
  Downstream – absolutely possible; just needs to be done
  Upstream – needs careful design
Effects of offset coils – needs to be considered in every study (still recommended)
Tolerable vacuum level determination – beamline backgrounds (Cip’s talk)
Dipole field specification – depends somewhat on some of the things above
Field measurement system needs
Continued iteration with JLAB and MIT engineers
Not started
Deprioritized
In progress
Done

## Slide 23: Fields produce desired particle tracks
Tracks are 6 and 21 mrads for both ep and mollers, from 3 different parts of the target
ep
moller
Side view of =0 field and tracks (center of open septant)
Tracks have energy/angle correlation, but not the radiative effects in the target
detector plane z=2650cm
Red – “open” sector
Blue – closed sector
Green – transition sector
1D radial dist., all
includes rad. eff.
2D rate
Dashed lines indicate the extent of a single septant
Transport through the magnets causes the moller “envelope” to be azimuthally defocussed
The add’l segmentation in moller ring allows for monitoring of systematics
Require 20% less up to 10% higher current for background determination
Notes: This slide shows another contour plot showing the relative total field at the center of an open sector in a plane parallel to the beamline. Superimposed are two sets of particle tracks produced in TOSCA; one for the electrons from elastic ep scattering and the moller electrons. In the lower right is a 1D distribution of these events from the GEANT simulation which includes all the radiative effects in the target. You see the long radiative tail from the elastic events underneath the MOLLER peak is approximately flat; to minimize this and the inelastic background we want as tight a focus in the moller peak as we can get.

## Slide 24: Ultra-precise measurement of weak mixing angle Standard Model Test
High precision yields a weak mixing angle measurement to test the Standard Model
  Need a high beam current, high polarization and a long target
  Maximize the acceptance while minimizing backgrounds
Identical particle scattering
  Achieve full acceptance by detecting the “other” electron in opposite septant
  Results in a large range of energies and angles in lab frame
Special considerations
  “No” iron in the magnet or collimators (parity experiment)
  Limited space to fit the conductor
  Understanding of backgrounds including the dilution (rate fraction) and asymmetry
The signal is an asymmetry
from e-e- scattering
Notes: The high precision of the MOLLER experiment is key to testing the Standard Model. So we need a high current, highly polarized beam and a long target. In addition, we want to have the biggest acceptance we can have with tolerable backgrounds. We benefit from the fact that our signal is from single particle scattering (more on the next slide) to achieve full azimuthal acceptance around 90 degrees in the center of mass, which results in a large range of lab scattering angles and energies.
In addition, we want to exclude any magnetic materials and fit the experiment in the hall, because this is a parity experiment and our signal is an asymmetry; iron has a large analyzing power. We also need to minimize background rate fractions but also be able to determine their asymmetries.

## Slide 25: Epoxy shielding is being optimized to reduce the weight of the shielding
Upstream torus
  shielding is sufficient – optimizing to reduce weight of 2-bounce shield
Downstream Torus
  shielding configuration works for the asymmetric coil configs
  expected stresses may be low enough for 100 MGy integrated dose
  only stresses present during operation matter wrt the dose
Check dose for G10 filler material density in the simulation

## Slide 26: Engineering designed to meet the physics requirements
The spectrometer system must
  Achieve the physics optics (bend particles) by
    defining the angular acceptance in a well-defined way
    separating the moller and elastic ep electrons
    providing 3 kinematic regions of the inelastic electrons (to deconvolve the asymmetries)
  Shield the experiment by
    minimizing the backgrounds at the detector
    reducing the conductor epoxy and G10 filler dose from excessive radiation to acceptable levels
    ensuring clean transport of the primary beam to the dump
  Operate for a long running time (344 PAC days)
The acceptance of the moller electrons is defined at collimator 2
The shape of the coils and the specified tolerances achieve the physics optics
Field stability requirements modest due to averaging over time and cancellation b/c measuring asymmetry
Collimator 1 defines the primary beam through experiment to the dump
Coils and supports obey > 5x multiple scattering radius by design
The collimators, lintels and beam shields are all designed to minimize the backgrounds at the detector plane
The shielding is being optimized to shield the coil epoxy/ G10 filler as well to maintain shear strength

## Slide 27: 100% Azimuthal Acceptance Possible
2 < E’ < 8 GeV
6 < θ < 21 mrads
21 mrad
6 mrad
9.5 mrad
e-
e-
e-
e-
Any odd number of coils will allow for 100% acceptance
e-
e-
Lab Frame
Coils in closed sectors
Detectors in open sectors
Forward and backward (in COM) scattered electrons from two events (line type links electrons from same event)
Need to shield conductors/ supports
Energy and scattering angle strongly correlated for mollers (eps are all ~11 GeV)
Maximize azimuthal acceptance
  identical particle scattering
  accept COM angles around 90◦
Large energy and angle range to focus
Acceptance defining collimator
Appendix

## Slide 28: Shape of Field in a Septant – varies along z, and also along r and
in the direction
azimuthal de-focusing
Vector map colors show relative total field strength in a septant
Radial components of field cause azimuthal (de-)focussing near the conductor at the (outer) inner radius of the conductor
  Provides required inelastic electron separation
  Causes mid-angle mollers to fill full azimuth at detector
Field varies along z to separate the low E moller and high E eps
BMOD
Bφ
Bz
B (Gauss)
z=9500mm
R=135mm
z=9500mm
azimuthal focusing
Appendix
Notes: This contour plot shows the relative strength of the total field in different locations within a septant. The approximate locations of the adjacent coil cross-sections are shown in orange. Illustrative field vectors indicate the direction of the field at different places. The radially focussing part of the field is the phi component; at the center of the septant the field is all in the phi direction. Near the coils, however, you have components in the radial direction. In between the inner radius parts of the coil, this results in azimuthal focussing of electrons; in between the outer radius parts of the coils we get phi defocussing. We make use of the focussing in phi to study the different parts of the acceptance.

## Slide 29: Stray fields in beampipe deflect e±
Consider the horizontal coil, in the perfectly symmetric case
all velocity in the z-direction
field is vertical along the x axis, (mid-plane of coil)
just off the axis,
  the field direction is dramatically different
e- will be bent to the right
e+ will be bent to the left (onto the coil)
  e± would feel both horizontal and vertical components of force
  dispersed
e-
e+
10-6
Worst case scenario
Appendix

## Slide 30: Downstream Coil B Dose (MGy)
Symmetric, no shield
Symmetric, w/ shield
+/- 1 or 3 mm offset, w/ shield
+/- 0.5 mm offset, w/ shield
Symmetric, Kryptonite* shield
* “Kryptonite” stops all tracks that hit it.
+/- 1 or 3 mm offset, no shield
Appendix

## Slide 31: Using the whole detector array
Although we call the rings moller or ep rings, we actually use more than one ring to determine the moller asymmetry
We will use the different contributions of the rate and asymmetry for each of the processes in each of the detector tiles to “deconvolute” the asymmetries for each process
Measurements to benchmark simulation with tracking system
  low current runs - rate distribution on array
  alternate beam energies
  neutral dilution determination
high current - vary magnet currents to see how rates changes from quartz to quartz (20% less up to 10% higher current)
Appendix
Notes: we will also take measurements with the tracking system triggered on the main detectors (or even pulser triggered), where the GEMs and the trigger scintillators can then reject charged particles in software, and we can get at the pure neutral dilution directly

## Slide 32: Sector Orientation
Closed sector to beam left to shield synchrotron radiation from hall A arc
Horizontal coil
Appendix

## Slide 33: Finite Target Effects - Example
ztarg,up = | -75 | cm
ztarg,center = | 0 | cm
ztarg,down = | 75 | cm
Rinner = | 3.658 | cm
Router = | 11.306 | cm
θlow,cen = | 6.2 | mrads | 
θhigh,cen = | 19.2 | mrads | 
Rinner
Router
ztarg,down
ztarg,up
ztarg,center
θlow,up
θlow,down
θhigh,up
θhigh,down
Expected Q2 distribution
zcoll = | 590 | cm
θlow = | 5.5 | mrad
θhigh = | 17 | mrad
 | θlow,down = | 7.1 | mrads
 | θhigh,down = | 21 | mrads
The acceptance varies along the length of the target
Requires mapping with the tracking system
Appendix

## Slide 34: Backups
Backups related to the SRD, things that are still TBD or TBR
Backups for the numbers that are solid if possible

## Slide 35: Nominal (symmetric) case – clean transport to dump
Looking upstream
Looking downstream
symmetric
In the top left plot you see a picture of the ds coils at a particular z location with the magnetic field contours and vectors
Middle top plot is a 2D rate distribution at the entrance to the dump tunnel
To the right is a 1D distribution of the rate in horizontal septant (1); the vertical lines indicate the radius of various apertures
Rate distribution for a slice along radius
Limiting aperture in dump tunnel
(~0.5 m downstream)
Dump entrance flange
(same z location as plots)
Beampipe intrusion for the SAMs
(~0.5m upstream)
Symmetric coils, w/o SAMs
Notes: Next steps are to look deeper into the dump to de

## Slide 36: Worst case – clean transport to dump
Worst case scenario
Looking upstream
Looking downstream
Limiting aperture in dump tunnel
(~0.5 m downstream)
Rate distribution for a slice along radius
In the top left plot in the worst case scenario there is an induced dipole field > 100 G over most of the area inside the coils
In this particular orientation, the electrons are bent upward into septant 2
To the right is a 1D distribution of the rate in the worst septant (2); even in the worst-case scenario the beam is mostly clearing
Dump entrance flange
(same z location as plots)
Beampipe intrusion for the SAMs
(~0.5m upstream)
Case 1, no SAMs/shield
Notes: Next steps are to look deeper into the dump to de

## Slide 37: Comparison of cases – clean transport to the dump
Case 1
Case 3
Case 2
Most likely
Symmetric coils, no SAMs
Case 1, no SAMs/shield
Symmetric coils, w/ SAMs
Case 2, w/ SAMs/shield
Case 3, w/ SAMs/shield
38.1 W
260 W
13.4 W
17.8 W
14.2 W
Symmetric coils, no SAMs
Case 1, no SAMs/shield
Symmetric coils, w/ SAMs
Case 2, w/ SAMs/shield
Case 3, w/ SAMs/shield
Integrated Power from 200 mm < r < 600 mm
Total Beam Power 715 kW
Symmetric coils, w/ SAMs
worst case is 10-4 of total beam power
order of magnitude lower for most likely case

## Slide 38: Fields along φ @ z=1350 cm for different r
Br(9 cm)
z = 1350 cm
Appendix
Bφ(13.5 cm)
Br(29 cm)
Br(13.5 cm)

## Slide 39: Fields along r @ z= 1350 cm
BMOD
Bø
Br
BMOD
Bø
Br
z = 1350 cm
center of open
z = 1350 cm
edge of open
Appendix

## Slide 40: Fields along z @ r = 13.5 cm
BMOD
Bz
Bz at edge
Bz center
r = 13.5 cm
center of open
r = 13.5 cm
edge of open
non-zero z components near current returns (included in field maps)
Appendix

## Slide 41: 2 bounce code
Python code
  Target, collar, collimators, beam shields, detector (600, 690-1300 mm)
  Uses straight lines to simulate an isotropic source (with random position, angle)
  Surfaces that “see” the target (red) become new sources
Tolerance study
  move the collimators and/or coils by +/- 1 mm w/o seeing green on the detectors
  1-bounce source
  sees 1-bounce from target
  sees the target
  Proper beam shield
Appendix

## Slide 42
Sol11 – 600 cm < z < 1700 cm, 10 A/mm2
Sol12 – 600 cm < z < 1700 cm, 104 A/mm2
Hihi (1000 – 11000 MeV)
High (100 – 1000 MeV)
Mid (10 – 100 MeV)
Low (1 – 10 MeV)
0.4 mrad
Stray fields only, no solenoid

## Slide 43
Sol11 – 600 cm < z < 1700 cm, 10 A/mm2
Sol12 – 600 cm < z < 1700 cm, 104 A/mm2
Hihi (1000 – 11000 MeV)
High (100 – 1000 MeV)
Mid (10 – 100 MeV)
Low (1 – 10 MeV)
2.4 mrad
Stray fields only, no solenoid

## Slide 44
Sol11 – 600 cm < z < 1700 cm, 10 A/mm2
Sol12 – 600 cm < z < 1700 cm, 104 A/mm2
Hihi (1000 – 11000 MeV)
High (100 – 1000 MeV)
Mid (10 – 100 MeV)
Low (1 – 10 MeV)
3.4 mrad
Stray fields only, no solenoid

## Slide 45: Segmented vs. Hybrid Downselect
segmented
blockyHybrid
V1U.2a_V1DSg.3
V1U.2a_V2DHy
V1U.2a_V2DSg.1b
V1U.2a_V2DSg.1b
distributions at detector plane
moller
elastic
inelastic
See change control document