## Slide 1: Spectrometer physics
Fields and particle tracks
Juliette Mammei

## Slide 2: Open Spectrometer system separates signal from backgrounds
Coils in one septant
Acceptance defining collimator(s) – coll1+2
Full azimuthal acceptance for mollers from
6 < < 20 mrads
cleanup collimator – coll 4
Collimators 5 and 6a, b provide add’l clearance to coils
Photon scraper provides clearance to the photon envelopes
lintels and collars throughout to provide shielding for detectors
particle envelopes defined along beamline
Wedges and “2-bounce” tube to shield epoxy

## Slide 3: 100% Azimuthal Acceptance Possible
2 < E’ < 8 GeV
6 < θ < 21 mrads
21 mrad
6 mrad
9.5 mrad
e-
e-
e-
e-
Any odd number of coils will allow for 100% acceptance
e-
e-
Lab Frame
Coils in closed sectors
Detectors in open sectors
Forward and backward (in COM) scattered electrons from two events (line type links electrons from same event)
Energy and scattering angle strongly correlated for mollers (eps are all ~11 GeV)
Maximize azimuthal acceptance
  identical particle scattering
  accept COM angles around 90◦
Large energy and angle range to focus
Acceptance defining collimator
Appendix

## Slide 4: Shape of Field in a Septant – varies along z, and also along r and
in the direction
azimuthal de-focusing
Vector map colors show relative total field strength in a septant
Radial components of field cause azimuthal (de-)focussing near the conductor at the (outer) inner radius of the conductor
  Provides required inelastic electron separation
  Causes mid-angle mollers to fill full azimuth at detector
Field varies along z to separate the low E moller and high E eps
BMOD
Bφ
Bz
B (Gauss)
z=9500mm
R=135mm
z=9500mm
azimuthal focusing
Appendix
Notes: This contour plot shows the relative strength of the total field in different locations within a septant. The approximate locations of the adjacent coil cross-sections are shown in orange. Illustrative field vectors indicate the direction of the field at different places. The radially focussing part of the field is the phi component; at the center of the septant the field is all in the phi direction. Near the coils, however, you have components in the radial direction. In between the inner radius parts of the coil, this results in azimuthal focussing of electrons; in between the outer radius parts of the coils we get phi defocussing. We make use of the focussing in phi to study the different parts of the acceptance.

## Slide 5: Fields produce desired particle tracks
Tracks are 6 and 21 mrads for both ep and mollers, from 3 different parts of the target
ep
moller
Side view of =0 field and tracks (center of open septant)
Tracks have energy/angle correlation, but not the radiative effects in the target
detector plane z=2650cm
Red – “open” sector
Blue – closed sector
Green – transition sector
1D radial dist., all
includes rad. eff.
2D rate
Dashed lines indicate the extent of a single septant
Transport through the magnets causes the moller “envelope” to be azimuthally defocussed; allows for
  monitoring of systematics
  deconvolution of the asymmetries
Require ± 10% current for background determination
Notes: This slide shows another contour plot showing the relative total field at the center of an open sector in a plane parallel to the beamline. Superimposed are two sets of particle tracks produced in TOSCA; one for the electrons from elastic ep scattering and the moller electrons. In the lower right is a 1D distribution of these events from the GEANT simulation which includes all the radiative effects in the target. You see the long radiative tail from the elastic events underneath the MOLLER peak is approximately flat; to minimize this and the inelastic background we want as tight a focus in the moller peak as we can get.

## Slide 6: Blocking backgrounds (and not signal!) – ray drawing
Collimators
1+2 4
Inner Photon Envelope
ep
Target
Lintels
Collars
Detector plane
moller
Ray traces with apertures
Coils shown for position reference (actually in closed sector)
Moller/ep
Line of sight
DS beampipe between OPE and ep envelopes
Outer Photon Envelope

## Slide 7: Beam particles with various energies and scattering angle of 2.4 mrad
Collimators
1+2 4
Inner Photon Envelope
ep
Target
Lintels
Collars
Detector plane
moller
Ray traces with apertures
Coils shown for position reference (actually in closed sector)
Rays for “primary beam” particles of different energies for a relatively large angle
Moller/ep
Line of sight
DS beampipe between OPE and ep envelopes
Outer Photon Envelope

## Slide 8: Fields in the beamline – symmetric and asymmetric cases
dump entrance
flange (r = 483 mm)
limiting aperture in dump tunnel (r=300mm)
(~0.5 m downstream)
End of Hall
electrons
(within tolerances)
Worst case scenario
dipole field
Consider the horizontal coil, in the perfectly symmetric case
all velocity in the z-direction
field is vertical along the x axis, (mid-plane of coil)
just off the axis,
  e± would feel both horizontal and vertical components of force
  the field direction is dramatically different
  dispersed
e+ will be bent to the left (onto the coil)
e- will be bent to the right (into the open sector)

## Slide 9: Alignment tolerances determined first by physics and clearance of signal
along z
Tolerances determined by single coil/single offset studies have been verified with “worst-case” multiple coil/multiple offsets within the specified tolerances
Considerations
  physics optics (ability to “deconvolute” the asymmetries with desired uncertainty)
    signal electron focal plane distributions
    backgrounds
  clearance with the scattered particle envelopes
  clean transport to the dump
  doses on coils (epoxy, especially at inner radius)
radially
azimuthally
Physics worst case
All coils offset in same direction (without us knowing)
Least likely (survey, tracking)
Relatively insensitive
single coil/ single offset tolerances
BEAM worst cases tested
coils aligned in a “conspiratorial” way within tolerances
→ induces dipole along beamline
worst (to left)
more likely - only ±0.5 mm
most likely ±0.5 mm and random for different subcoils

## Slide 10: Summary
Many spectrometer items are actually here, at the lab (see engineers talks)
Many things are being tested for quality control and as-built dimensions for entry into the simulations
Eventually as-built coil maps will be produced
The optics group is looking into the effects of offset coils and the ability to verify coil locations using tracking data (see optics talks)
People should be aware of the effects of the field on electrons (and positrons) in both the acceptance region and the beamline
When simulating you should consider using the symmetric map and also asymmetric maps, especially if considering beamline backgrounds

## Slide 11: Appendix

## Slide 12: Shape of Field in a Septant – varies along z, and also along r and
in the direction
azimuthal de-focusing
Vector map colors show relative total field strength in a septant
Radial components of field cause azimuthal (de-)focussing near the conductor at the (outer) inner radius of the conductor
  Provides required inelastic electron separation
  Causes mid-angle mollers to fill full azimuth at detector
Field varies along z to separate the low E moller and high E eps
BMOD
Bφ
Bz
B (Gauss)
z=9500mm
R=135mm
z=9500mm
azimuthal focusing
Appendix
Notes: This contour plot shows the relative strength of the total field in different locations within a septant. The approximate locations of the adjacent coil cross-sections are shown in orange. Illustrative field vectors indicate the direction of the field at different places. The radially focussing part of the field is the phi component; at the center of the septant the field is all in the phi direction. Near the coils, however, you have components in the radial direction. In between the inner radius parts of the coil, this results in azimuthal focussing of electrons; in between the outer radius parts of the coils we get phi defocussing. We make use of the focussing in phi to study the different parts of the acceptance.

## Slide 13: Using the whole detector array
Although we call the rings moller or ep rings, we actually use more than one ring to determine the moller asymmetry
We will use the different contributions of the rate and asymmetry for each of the processes in each of the detector tiles to “deconvolute” the asymmetries for each process
Measurements to benchmark simulation with tracking system
  low current runs - rate distribution on array
  alternate beam energies
  neutral dilution determination
high current - vary magnet currents to see how rates changes from quartz to quartz (20% less up to 10% higher current)
Appendix
Notes: we will also take measurements with the tracking system triggered on the main detectors (or even pulser triggered), where the GEMs and the trigger scintillators can then reject charged particles in software, and we can get at the pure neutral dilution directly

## Slide 14: Sector Orientation
Closed sector to beam left to shield synchrotron radiation from hall A arc
Horizontal coil
Appendix

## Slide 15: Finite Target Effects - Example
ztarg,up = | -75 | cm
ztarg,center = | 0 | cm
ztarg,down = | 75 | cm
Rinner = | 3.658 | cm
Router = | 11.306 | cm
θlow,cen = | 6.2 | mrads | 
θhigh,cen = | 19.2 | mrads | 
Rinner
Router
ztarg,down
ztarg,up
ztarg,center
θlow,up
θlow,down
θhigh,up
θhigh,down
Expected Q2 distribution
zcoll = | 590 | cm
θlow = | 5.5 | mrad
θhigh = | 17 | mrad
 | θlow,down = | 7.1 | mrads
 | θhigh,down = | 21 | mrads
The acceptance varies along the length of the target
Requires mapping with the tracking system
Appendix

## Slide 16: Stray fields in beampipe deflect e±
Consider the horizontal coil, in the perfectly symmetric case
all velocity in the z-direction
field is vertical along the x axis, (mid-plane of coil)
just off the axis,
  the field direction is dramatically different
e- will be bent to the right
e+ will be bent to the left (onto the coil)
  e± would feel both horizontal and vertical components of force
  dispersed
e-
e+
10-6
Worst case scenario
Appendix

## Slide 17: Clean transport to dump even in worst asymmetric coils*
W/µA/(1mm x 1mm)
dump entrance
flange (r = 483 mm)
limiting aperture in dump tunnel (r=300mm)
(~0.5 m downstream)
SAM pipe
OD 400 mm
End of Hall
electrons
38.1 W
260 W
13.4 W
17.8 W
14.2 W
Symmetric coils, no SAMs
Case 1, no SAMs/shield
Symmetric coils, w/ SAMs
Case 2, w/ SAMs/shield
Case 3, w/ SAMs/shield
Integrated Power from 200 mm < r < 600 mm
Total Beam Power 715 kW
Coil Configuration
(most likely configuration)
worst-case* asymmetric coils
(within tolerances)
Worst case scenario
*case 1, slide 7
dipole field

## Slide 18: Collimators define acceptances and shielding protects equipment
Wedges and “2-bounce” tube to shield US torus epoxy
Collimator 4 similar to 2 – “cleanup collimator” – at the end of the US enclosure
Downstream region
Collimator 2 defines angular acceptance for signal
Collimator 1 inserted into 2 to shield end
Upstream Region
Collimators 5 and 6a, b provide additional clearance to coils
lintels and collars provide shielding for detectors
Photon scraper provides clearance to the photon envelopes

## Slide 19: Ferrous Materials - Spectrometer
Double-spin ee or γe scattering from ferrous material can have large asymmetry.
In ~1G ambient field:
mild steel: Ps~10-2
Stainless steel: Ps~10-5 ~10-7
Inconel 625: Ps ~10-8
Aluminum (paramagnetic): Ps <10-9
Estimate false asymmetry
fr rate fraction of process
Pe incident electron polarization
Ps material electron polarization
An analyzing power
Goal: Af < 10-11
Guidance for engineering, using conservative estimates of PeAn ~10-3
Simulations in G4, using ad hoc “biasing” for rare event estimation
Examples in spectrometer system:
Large diameter bellows 4 was specified to be built using SS 316 or 310, with 310 weld rods. Bellows 1-3 were allowed to be SS, Bellows 5 and 7 are Inconel. This controlled technical risk without excessive cost.
Tie rod ends for coil assembly support: large number of ferrous hardware were shown to be unacceptable - to be replaced by titanium
Demonstrated need for silicon bronze fastener hardware on coils mounts
Approved SS vacuum or water connections at edge of spectrometer
Demonstrated need for concrete walls downstream of US Torus and drift pipe due to floor-level ferrous steel

## Slide 20: Engineering designed to meet the physics requirements
The spectrometer system must
  Achieve the physics optics (bend particles) by
    defining the angular acceptance in a well-defined way
    separating the moller and elastic ep electrons
    providing 3 kinematic regions of the inelastic electrons (to deconvolve the asymmetries)
  Shield the experiment by
    minimizing the backgrounds at the detector
    reducing the conductor epoxy/G10 filler dose from excessive radiation to acceptable levels
    ensuring clean transport of the primary beam that has gone through the target to the dump
  Operate for a long running time (344 PAC days)
The acceptance of the moller electrons is defined at collimator 2
The shape of the coils and the specified tolerances achieve the physics optics
Field stability requirements modest due to averaging over time and cancellation b/c measuring asymmetry
Collimator 1 defines the primary beam through experiment to the dump
Coils and supports obey >5x multiple scattering radius by design
The collimators, lintels and beam shields are all designed to minimize the backgrounds at the detector plane
The shielding is optimized to shield the coil epoxy/ G10 filler as well to maintain shear strength